## Slide 1: Computerized Dance Classroom
Using kinect to evaluate dance performances
Stylianos venieris
Marcin baginski
Theo pavlakou
Hesam ipakchi
Zeping xue
Yijie ge

## Slide 2: Project Background
RGB-D cameras:
  Microsoft Kinect
  Asus Xtion
  other
OpenNI
NiTE
Notes: An emergence of RGB-D cameras, such as Microsoft Kinect or Asus Xtion, has lead a development of applications with a completely new type of user interaction
With an RGB-D camera, users are not required to hold any controllers in their hands, but perform gestures in front of the camera, which are automatically interpreted by the device

## Slide 3: Outline
Project Aims
Evaluation of Kinect, OpenNI and NiTE
Automatic Scoring System
  Motionless Activity Detector
  Translation Module
  Data Alignment Module
  Data Analysis Module
Application and its features
Extensions
Commercial Aspect

## Slide 4: Project Aims
Bring Kinect technology to a dance classroom
Evaluate tracking capabilities of Kinect, OpenNI and NiTE
Develop software for recording dance performances
Create algorithms for automatic recognition of errors and comparison of two dance movements
Make the application user friendly

## Slide 5: Evaluation of Kinect, OpenNI and NiTE
Camera range:
  60 cm – recognises subjects
  120 cm – starts tracking
  410 cm – stops tracking
Lighting conditions:
  No effect on the tracking capabilities
Velocity of movement
  Faster movement can decrease the precision of data returned from NiTE
Camera angle relative to the performers
  If a person stands at a 90° to the camera, it can lose tracking of the limbs which are covered by the body

## Slide 6: Evaluation of Kinect, OpenNI and NiTE
Interference between multiple cameras
  Careful placement of cameras can minimise the interference
Occlusion in front of the camera
  Creates a problem, camera loses tracking if a part of the body is covered by an object
Number of tracked people
  In theory constrained only by how many can actually fit in the camera range
  In practise, inevitable occlusion between multiple people limits the number to about 2

## Slide 7: Automatic Dance Scoring - System
Main purpose of the system – compare and score the student’s performance with respect to the teacher’s
Divided into four manageable modules, where the output of the former is the input of the latter
Motionless Activity Detector
Translation Module
Data Analysis Module
Data Alignment Module
Dance
Score

## Slide 8: Automatic Dance Scoring – Motionless Activity Detector
Motionless Activity Detector
  Before performing any movement, the person needs to stand still for approx. 2 s for the software to calibrate
  Motionless Activity Detector returns a frame number in the recording where the person was not moving

## Slide 9: Automatic Dance Scoring – Translation Module
Translation Module
  Takes the frame number from the Motionless Activity Detector and discards all the data which happened before this frame
  Additionally, ‘normalises’ the data, such that the exact position of the subject in the camera range not included any more
Before
After

## Slide 10: Automatic Dance Scoring – Data Alignment Module
Data Alignment Module
  Even after translation, there is still a possibility of misalignment between the data of two dance moves
  Data Alignment Module aims to bring the two signals to as close alignment as possible
After
Before

## Slide 11: Automatic Dance Scoring – Data Analysis Module
Data Analysis Module

## Slide 12: The Application

## Slide 13: The Application
Screenshots?
Features

## Slide 14: The Application
Screenshots?
Features

## Slide 15: Extensions
Machine learning

## Slide 16: Limitations

## Slide 17: Commercial Aspect

## Slide 18: Summary