## Slide 1: Computerized Dance Classroom
Using kinect to evaluate dance performances
Stylianos venieris
Marcin baginski
Theo pavlakou
Hesam ipakchi
Zeping xue
Yijie ge

## Slide 2: Project Background
RGB-D cameras:
  Microsoft Kinect
  Asus Xtion
  other
OpenNI
NiTE
Notes: An emergence of RGB-D cameras, such as Microsoft Kinect or Asus Xtion, has lead a development of applications with a completely new type of user interaction
With an RGB-D camera, users are not required to hold any controllers in their hands, but perform gestures in front of the camera, which are automatically interpreted by the device

## Slide 3: Outline
Project Aims
Evaluation of Kinect, OpenNI and NiTE
Automatic Scoring System
  Motionless Activity Detector
  Translation Module
  Data Alignment Module
  Data Analysis Module
Application and its features
Extensions
Commercial Aspect

## Slide 4: Project Aims
Bring Kinect technology to a dance classroom
Evaluate tracking capabilities of Kinect, OpenNI and NiTE
Develop software for recording dance performances
Create algorithms for automatic recognition of errors and comparison of two dance movements
Make the application user friendly

## Slide 5: Evaluation of Kinect, OpenNI and NiTE
Camera range:
  60 cm – recognises subjects
  120 cm – starts tracking
  410 cm – stops tracking
Lighting conditions:
  No effect on the tracking capabilities
Velocity of movement
  Faster movement can decrease the precision of data returned from NiTE
Camera angle relative to the performers
  If a person stands at a 90° to the camera, it can lose tracking of the limbs which are covered by the body

## Slide 6: Evaluation of Kinect, OpenNI and NiTE
Interference between multiple cameras
  Careful placement of cameras can minimise the interference
Occlusion in front of the camera
  Creates a problem, camera loses tracking if a part of the body is covered by an object
Number of tracked people
  In theory constrained only by how many can actually fit in the camera range
  In practise, inevitable occlusion between multiple people limits the number to about 2

## Slide 7: Automatic Dance Scoring - System
Main purpose of the system – compare and score the student’s performance with respect to the teacher’s
Divided into four manageable modules, where the output of the former is the input of the latter
Motionless Activity Detector
Translation Module
Data Analysis Module
Data Alignment Module
Dance
Score

## Slide 8: Automatic Dance Scoring – Motionless Activity Detector
Motionless Activity Detector
  Before performing any movement, the person needs to stand still for approx. 2 s for the software to calibrate
  Motionless Activity Detector returns a frame number in the recording where the person was not moving
Input
Output

## Slide 9: Automatic Dance Scoring – Translation Module
Translation Module
  Takes the frame number from the Motionless Activity Detector and discards all the data which happened before this frame
  Additionally, ‘normalises’ the data, such that the exact position of the subject in the camera range not included any more
Input
Output

## Slide 10: Automatic Dance Scoring – Data Alignment Module
Data Alignment Module
  Even after translation, there is still a possibility of misalignment between the data of two dance moves
  Data Alignment Module aims to bring the two signals to as close alignment as possible
Input
Output

## Slide 11: Automatic Dance Scoring – Data Analysis Module
Data Analysis Module
  Takes two aligned signals and produces a score as the output
  Produces an average score for the entire dance as well as a windowed score for each of the 10 parts of the dance, each of equal duration
  The scores are calculated for each coordinate and joint
Input
Output

## Slide 12: The Application

## Slide 13: Extensions
Teacher-defined level of importance for each part of the student’s body during a dance
  Already implemented and integrated in the application
Use of a machine learning algorithm to derive a scoring scheme based on dance instructors’ metric
  Prototype implemented and tested in Matlab
Use of multiple cameras to improve the overall accuracy
  Substantial obstacles due to calibration and tracking overhead

## Slide 14: Limitations
Tracking limitations of Kinect, OpenNI and NiTE
  Range, velocity of movement, time for calibration
  OpenNI supports only one camera on one computer
Partner dances not supported
  Due to inevitable occlusion which distorts the data
Height differences
  Significant differences in height increase the error
Specific instructions must be followed by the user
  e.g. the dancer needs to stand still for approx. 2 s before dancing

## Slide 15: Commercial Aspect – solving the problem
Lack of specific feedback for students in large groups
  The application provides student-specific feedback and can keep track of the student’s progress
Must travel to a physical destination to practise
  The application allows to practise at any time and in any place, therefore beneficial for both students and teachers
Expensive
  By increasing the number of students per teacher and decreasing the time that needs to be devoted physically to each student, the application can significantly reduce the cost of learning to dance
Notes: Problem definition: teacher – students ratio.
- Approach a ratio of 1
- More accurate student-specific and dance-specific (see weightings) feedback
- Homework
- Possible to revolutionize dance classrooms
Possible extension to online courses (eg online guitar courses)
Automated, reliable marking (trained by professionals)
- Can be extended to other activities (martial arts, aerobics, etc)

## Slide 16: Commercial Aspect – business model
The core version of the software acquired by teachers and students for a fixed price - £100
Teachers have access to a cloud space where they can upload their videos
Students can obtain the dances from the online store where they can choose to download their teacher’s videos or videos uploaded by others for a small fee
The software needs initially 3 people for maintenance purposes – 2 developers and 1 customer support

## Slide 17: Conclusion
Available hardware (Kinect) and software (OpenNI, NiTE) can be successfully used, subject to limitations
The prototype application includes:
  Recording of dance movements
  Playback of the recorded videos
  Recognising and overlaying skeletons on each other
  Automatically scoring two dance moves
We believe that the product can be successfully commercialised after beta testing in the real environment